## Slide 1
APPLIED ARTIFICIAL INTELLIGENCE
SHRIKE NANO
AI-Enabled sUAS Targeting for Digital Fires
CW2 Ali Baharanyi, Army AI2C | Greg Tozzi, Booz Allen Hamilton
GVSETS 2026 | Applied Artificial Intelligence | August 11–13, 2026 | Novi, Michigan
DISTRIBUTION STATEMENT A. Approved for public release; distribution is unlimited.
Notes: Welcome the audience. Introduce Shrike Nano and the 3/101 field integration effort. Thank NDIA Michigan Chapter and GVSETS organizers.

## Slide 2
APPLIED ARTIFICIAL INTELLIGENCE
Agenda
01
Problem & motivation
05
Field evaluation
02
Shrike Nano system overview
06
Performance results
03
Digital fires integration architecture
07
Lessons learned
04
AI-enabled targeting pipeline
08
Conclusions
GVSETS
GROUND VEHICLE SYSTEMS ENGINEERING & TECHNOLOGY SYMPOSIUM | 2026
NDIA Michigan Chapter
Notes: Walk through the arc of the talk: problem, system, architecture, AI pipeline, field test with 3/101, results, lessons, conclusions.

## Slide 3
APPLIED ARTIFICIAL INTELLIGENCE
The Targeting Gap
Traditional forward observer processes rely on manual target identification, voice communications, and disjointed systems, increasing cognitive load and delaying fire missions.
The proliferation of small unmanned aircraft systems (sUAS) at the tactical edge, creates a need to integrate aerial sensing directly into digital fires networks.
SHRIKE NANO CLOSES IT
Enables forward observers to detect, geolocate, and engage targets using sUAS video integrated within the Android Tactical Assault Kit (TAK) ecosystem, connected to AFATDS.
Supports "Find, Fix, Finish" across the targeting cycle.
GVSETS
GROUND VEHICLE SYSTEMS ENGINEERING & TECHNOLOGY SYMPOSIUM | 2026
NDIA Michigan Chapter
Notes: Explain the gap: manual FO workflows are slow and disjointed; sUAS are proliferating at the tactical edge but not wired into digital fires.

## Slide 4
APPLIED ARTIFICIAL INTELLIGENCE
System Overview
Shrike Nano is a body-worn, rapidly deployable targeting aid for forward observers and drone operators. Shrike Nano enables single-operator, sUAS-enabled digital fires workflows on a tactical smartphone.
sUAS Sensing
Real-time video & telemetry from small unmanned aircraft
Edge Compute
On-device target detection and passive geolocation
TAK Interface
Operator interface for target designation on the COP
Fires Network
Digital call-for-fire generation into AFATDS
Ingests video from platforms such as the Skydio X10D and PDW C100 via UAS Tool. The Shrike Nano ATAK plugin runs AI-assisted threat recognition on the feed.
GVSETS
GROUND VEHICLE SYSTEMS ENGINEERING & TECHNOLOGY SYMPOSIUM | 2026
NDIA Michigan Chapter
Notes: Describe Shrike Nano as a portable, single-operator targeting aid that runs on existing FO hardware inside TAK.

## Slide 5
APPLIED ARTIFICIAL INTELLIGENCE
Closed-Loop Targeting Architecture
sUAS Video & Telemetry
Skydio X10D / PDW C100
→
ATAK UAS Tool
RTSP → image/metadata pairs
→
Shrike Nano Plugin
AiTR + passive geolocation
→
ATAK COP
Operator designates target
→
Digital CFF (VMF)
via TSM / MUOS
→
AFATDS
Fire mission generation
This architecture lets the forward observer move directly from aerial reconnaissance to fire mission generation minimizing manual entry and shortening detect-to-fire timelines.
GVSETS
GROUND VEHICLE SYSTEMS ENGINEERING & TECHNOLOGY SYMPOSIUM | 2026
NDIA Michigan Chapter
Notes: Walk the closed-loop pipeline left to right: aircraft, UAS Tool, Shrike plugin with AiTR and geolocation, COP, operator designation, digital CFF, AFATDS via VMF.

## Slide 6
APPLIED ARTIFICIAL INTELLIGENCE
UAS Tool Integration
UAS Tool provides ground control of multiple aircraft platforms. It demultiplexes RTSP video into image–metadata pairs using native ATAK functionality.
By handling new-airframe integration, UAS Tool gives Shrike a platform-agnostic feed to ingest. Shrike picks up pairs from a last-in, first-out (LIFO) queue so the most recent image is always processed.
OPERATOR WORKFLOW
1
Fly aircraft via UAS Tool plugin to area of interest
2
Shift to Shrike plugin to identify and nominate targets
3
UAS Tool keeps running in background; aircraft stays under operator control via ground-control case
GVSETS
GROUND VEHICLE SYSTEMS ENGINEERING & TECHNOLOGY SYMPOSIUM | 2026
NDIA Michigan Chapter
Notes: Explain the division of labor between UAS Tool (flight/ground control) and Shrike (targeting), and the LIFO queue design.

## Slide 7
APPLIED ARTIFICIAL INTELLIGENCE
Aided Threat Recognition
AiTR assists operators in identifying potential targets from sUAS video, cutting cognitive load and reaction time. Operators could use it as a cueing aid, not the sole basis for nomination.
WHERE INFERENCE RUNS
On the operator's end-user device (EUD), using onboard GPU or NPU. Inference is typically the largest contributor to overall system cycle time.
FIDELITY vs. CYCLE TIME TRADEOFF
Higher-fidelity models detect more true positives; lower-fidelity models run faster and see more frames per unit time.
On-device AI inference continues to improve, but long-lived fielded mobile hardware creates heterogeneity, and low-bit quantization needs pipelines/data not always available in the field.
GVSETS
GROUND VEHICLE SYSTEMS ENGINEERING & TECHNOLOGY SYMPOSIUM | 2026
NDIA Michigan Chapter
Notes: Cover aided threat recognition: cueing not sole nomination, and the model fidelity vs cycle time trade-off driven by mobile inference hardware.

## Slide 8
APPLIED ARTIFICIAL INTELLIGENCE
Target Tracking & Geolocation
TRACKING
Detections are reported as Cursor on Target (CoT) messages. Associating new detections with prior tracks guards against saturating the COP.
Camera compensation and quadratic scaling with detection count make tracking a major cycle-time driver; Shrike offers multiple algorithms for tracking.
GEOLOCATION
Passive single-camera geolocation updates position each frame, tuned for area-effect weapons with commodity sensors, trading initial accuracy for algorithmic efficiency.
Benchmarked against observer visual estimates. Subsequent relative corrections are prioritized for accuracy; OEM implementation of position/attitude standards is occasionally uneven.
GVSETS
GROUND VEHICLE SYSTEMS ENGINEERING & TECHNOLOGY SYMPOSIUM | 2026
NDIA Michigan Chapter
Notes: Cover CoT-based tracking, data association across frames, and passive single-camera geolocation optimized for area-effect weapons.

## Slide 9
APPLIED ARTIFICIAL INTELLIGENCE
Field Evaluation with 3/101
Shrike Nano was integrated and tested within a Brigade Combat Team from the 101st Airborne Division (Air Assault) during training events at Fort Campbell, Kentucky.
Unit
3rd BCT, 101st Airborne Division (Air Assault)
Location
Fort Campbell, Kentucky
Events
Training exercises + CALFEX
Platform
Reconnaissance flights with the PDW C100
GVSETS
GROUND VEHICLE SYSTEMS ENGINEERING & TECHNOLOGY SYMPOSIUM | 2026
NDIA Michigan Chapter
Notes: Introduce the operational evaluation: integration with 3rd BCT, 101st Airborne at Fort Campbell, culminating in brigade-level CALFEX with the PDW C100.

## Slide 10
APPLIED ARTIFICIAL INTELLIGENCE
Geolocation Accuracy Results
Target location error (TLE) measured during reconnaissance flights with the PDW C100, at increasing range from the target:
Range <115 m
6 m
Target Location Error
Range <350 m
8 m
Target Location Error
Range <650 m
24 m
Target Location Error
Results validate the baseline capability of the passive geolocation algorithm, while highlighting the need for improved sensor metadata standardization and calibration across aircraft platforms.
GVSETS
GROUND VEHICLE SYSTEMS ENGINEERING & TECHNOLOGY SYMPOSIUM | 2026
NDIA Michigan Chapter
Notes: Present the geolocation accuracy data: TLE grows with range, validating baseline capability while showing the need for metadata standardization.

## Slide 11
APPLIED ARTIFICIAL INTELLIGENCE
Field Observations
WHAT WORKED
During CALFEX, Shrike Nano generated target coordinates and transmitted digital fire missions through AFATDS and MFCS.
Operators reported that generating target grids directly from aerial recon significantly reduced the cognitive workload of manual target development.
FRICTION POINTS
UAS range limitations, RF interference, aircraft firmware variability, and instability in some TAK software components.
These occasionally required operators to revert to voice communications or adjust procedures but never prevented mission execution.
GVSETS
GROUND VEHICLE SYSTEMS ENGINEERING & TECHNOLOGY SYMPOSIUM | 2026
NDIA Michigan Chapter
Notes: Cover the CALFEX success and the operational friction points: RF/range/firmware/software, and the strong operator confidence despite them.

## Slide 12
APPLIED ARTIFICIAL INTELLIGENCE
Lessons Learned
1
Systems engineering vs, software deployment
Failures anywhere across UAS, TAK, radios, or fires systems can interrupt the targeting workflow.
2
Metadata consistency is critical
KLV formatting and calibration variance across aircraft introduces geolocation inconsistencies.
3
Training methodology matters
Classroom instruction immediately followed by hands-on flight ops built proficiency fastest.
4
Network architecture is a key constraint
Digital fires exposes weaknesses in comms architectures. Close coordination with S-6 is of paramount importance.
GVSETS
GROUND VEHICLE SYSTEMS ENGINEERING & TECHNOLOGY SYMPOSIUM | 2026
NDIA Michigan Chapter
Notes: Walk through all four lessons: systems engineering framing, metadata consistency, training methodology, and network architecture constraints.

## Slide 13
APPLIED ARTIFICIAL INTELLIGENCE
Conclusions
Field experience shows Shrike Nano meets operational requirements for target detection, geolocation, and tracking within the constraints of existing indirect fires networks.
DECISION SUPPORT
AI-enabled digital fires, UAS feeds, and interoperable ATAK standards augment decisions in time-sensitive scenarios.
NETWORK PLANNING
Robust IP transport is a precondition for success — a shared challenge across systems, not unique to Shrike Nano.
A CASE STUDY
For AI-enabled TTPs that are faster, more responsive, and more lethal — while prioritizing warfighter survivability.
GVSETS
GROUND VEHICLE SYSTEMS ENGINEERING & TECHNOLOGY SYMPOSIUM | 2026
NDIA Michigan Chapter
Notes: Close with the case-study framing: Shrike Nano meets requirements, network planning is the precondition, and the broader mission is faster, more lethal, safer TTPs.