## Slide 1
Nelson Santini, Anoop Balakrishnan,
Michael Wagner
AI-Powered Safety Intelligence for Ground Vehicle MBSE

## Slide 2
The mandate is real. The measured benefit isn't — yet.
THE MBSE PROBLEM
DoDI 5000.97 (Dec 2023) requires program managers to implement digital engineering “to the maximum extent possible.” MBSE sits at the center of that vision. Here is what the assessments actually found:
<1%
of published literature actually quantified MBSE benefits — the rest merely perceived them
Defense Science Board, 2024
0
notable cost savings or schedule reductions attributable to digital engineering in industry survey
RAND industry survey, 2024
5 of 5
primary barriers to MBSE implementation were cultural, not technical
CMU SEI MBSynergy Workshop, 2025
The gap is not the modeling languages or the tools themselves — it is the manual burden the model-centric workflow places on engineers.

## Slide 3
If you run models on a program of record, you've lived this
THE MBSE PROBLEM
XM30 — the first fully model-based combat vehicle
A digital-engineering pathfinder, yet GAO (2025) linked schedule delays to MOSA non-compliance and to an assumption — which proved incorrect — that contractors were proficient in model-based methods. The architecture model grew far beyond what officials anticipated.
Model exchange that doesn't
Sequence diagrams exchanged via XMI arrived mostly empty and were rebuilt by hand. One DoD migration of 220,000 elements and 300 diagrams was judged a months-to-years task without specialized intervention.
Traceability lives in spreadsheets — and goes stale
Requirements → design → hazard analyses → V&V links are built manually, maintained inconsistently, and quietly rot between milestone reviews.
Multi-standard compliance, zero harmonization
MIL-STD-882E + DoDD 3000.09 + UL 4600, with more arriving as autonomy policy matures. Not contradictory, but each with its own terminology, process steps, and evidence expectations — and every one expects its artifacts kept current.
Sources: GAO-25-107569; Defense Science Board Task Force on Digital Engineering, 2024.

## Slide 4
The unnamed culprit: cognitive overload
THE MBSE PROBLEM
MBSE doesn't just digitize workflows — it forces explicit articulation of every relationship that used to live in engineers' heads.
Modify one safety requirement, and you must mentally propagate the change across five artifact families — in three or more disconnected tools — while satisfying several standards at once.
Parametric CAD followed the same arc in the 1990s: mandates preceded readiness, early use was slower than manual work, and adoption arrived only when the tool got out of the engineer's way.
Sustainable adoption requires actively reducing the cognitive load the toolchain imposes.
System hazard
analysis (882E)
Design elements
& interfaces
Verification
plan & tests
Safety case
argument node
Compliance artifacts
per standard
Upstream operational
need
ONE modified
safety requirement
…tracked manually, across 3+ tools, per standard

## Slide 5
“Just add AI”? First, name the culture clash.
SAFETY CONCERNS, HEAD-ON
Thomas & Wagner (SAE 2026) systematically analyzed LLM use across the safety-critical engineering lifecycle. The tension is not tooling — it's two communities weighting the same evidence differently.
The AI community
• Fueled by steep capability gains in a short time frame
• Places trust in the technology's trajectory
• Optimistically applies LLMs even to safety-critical engineering
• Customer pressure for “smarter” functionality amplifies the push
The safety community
• Socialized in stringent, well-established engineering processes
• Bound by the strictness of norms and standards
• Anxiously rejects LLMs as inadequate for safety-critical work
• Sees naïve pipelines bypassing artifacts that standards mandate
The way through combines both: the AI community's pace of technical improvement, bound by the safety community's proven process rigor and quality assurance.

## Slide 6
Not all LLM uses carry equal risk — classify first
SAFETY CONCERNS, HEAD-ON
Borrowing from established tool-qualification practice — DO-330 and its counterparts — Thomas & Wagner classify LLM-based tools by their ability to introduce or mask errors:
I2
Can introduce errors into the system
Requirements elicitation that misses or misstates requirements; generated source code with algorithmic errors; hazard analysis that omits hazards.
Highest qualification burden
I1
Can fail to detect errors
A consistency check that falsely reports a requirement set complete; generated test cases with inadequate coverage; wrong traceability links impeding verification.
Verification-masking risk
I0
No direct impact on results
Natural-language explanations of models or code for communication with non-engineering stakeholders; classification metadata.
Lowest rigor required
Role matters as much as impact: R2 tools automate or eliminate an engineering task; R1 tools assist a human who retains ownership. An I2 tool in an R2 role demands the most rigorous qualification — specification, compliance evidence, configuration management, evolution control — which today's LLM tools rarely meet.

## Slide 7
“A human will review it” is also a failure mode
SAFETY CONCERNS, HEAD-ON
Automation research from rail and aviation predicts what happens to engineers working alongside LLMs (Parasuraman & Riley; Thomas & Wagner):
Complacency & over-reliance
Highly reliable automation invites unjustified trust. Engineers lean on LLM output even where the tool is only meant to assist and responsibility remains human.
Skill fade
Engineers who no longer perform a task lose the ability to perform it — and with it, the ability to verify whether the LLM's result is correct.
Mistrust that erases savings
Visible errors drive perceived unreliability. Engineers re-verify everything at high effort, obliterating the efficiency the tool was bought to deliver.
Confusion & lost situational awareness
When engineers can't reconstruct why the LLM produced a result, they can't assess its correctness — producing unjustified trust or unjustified mistrust.
Consequence: even human-in-the-loop safeguards must be deliberately engineered, not assumed.

## Slide 8
The compliance trap: pipelines that vaporize your evidence
SAFETY CONCERNS, HEAD-ON
Naïve LLM pipeline — requirements straight to implementation
High-level
requirements
→
High-level design
(eliminated)
→
Detailed design
(eliminated)
→
Generated
code / model
No intermediate artifacts → no traceability, no unit-level test basis, no demonstration of absence of unintended behavior. Non-compliant at higher integrity levels.
Qualified model-based pipeline (SCADE-style) — the standards-sanctioned precedent
High-level
requirements
→
Formal model
= low-level reqs
→
Qualified code
generator
→
Source code,
fully traceable
Tasks are replaced, but every artifact exists — original or substitute — so traceability and verification survive. LLM tools must meet the same bar: automate individual tasks, never eliminate the artifacts.
Thomas & Wagner, SAE 2026 — comparison of LLM code generation vs. qualified model-based development.

## Slide 9
What responsible adoption requires
SAFETY CONCERNS, HEAD-ON
Thomas & Wagner are explicit: take the savings — under four conditions.
1
Qualify the tool
Analyze its impact class (I0–I2) and its role — assisting an engineer or automating a task — before use, exactly as for any other development tool.
2
Verify with rigor
Use only tools that can be qualified at the required level, or embed their output in verification of sufficient rigor — ideally tool-based, not just human eyes.
3
Keep engineers capable
The humans in the loop must remain able to verify what the tool produces. Oversight that can't check the work isn't oversight.
4
Keep the artifacts
Automate individual tasks; never eliminate intermediate artifacts. They are where traceability, verification, and standards compliance live.
The Digital Safety Twin was architected against exactly this bar.

## Slide 10
The Digital Safety Twin
THE APPROACH
A conventional digital twin mirrors the physical system. The Digital Safety Twin mirrors the safety reasoning — the live chain of logic from operational concept through hazards, requirements, mitigations, and evidence to the claim that the system is acceptably safe. Each of its three capabilities exists to retire a specific piece of the cognitive overload named earlier.
1
AI-driven requirements formalization
Hybrid NLP/LLM pipeline turns CONOPS, threat assessments, and engineering notes into structured, traceable candidate requirements — with a deterministic verification layer as guardrail.
2
Auto-generated traceability
A knowledge graph proposes and continuously maintains trace links across requirements, design, hazard analyses, and V&V — constrained by 882E, RAAML, and UL 4600 ontologies.
3
Continuous safety case assessment
A living GSN argument connected to live evidence, reporting structural completeness and Bayesian confidence — at any moment, not just at milestone reviews.
Grounded in STPA, OMG RAAML, MIL-STD-882E, and UL 4600. A methodological contribution — it augments qualified engineers, never replaces them.

## Slide 11
From unstructured documents to traceable requirements
CAPABILITY 1
LOAD LIFTED blank-page formalization
Programs run on prose — CONOPS, operational requirements, threat assessments, lessons learned. Converting it into formal requirements is today a manual, expert-intensive bottleneck.
WHAT IT DOES (ILLUSTRATIVE)
CONOPS §4.2 — prose
“Crew must be able to halt autonomous movement at any time, regardless of mission mode.”
→
REQ-SAF-041 · CANDIDATE
When the operator issues a halt command, the system shall bring the vehicle to a controlled stop within [TBD] s.
EARS event-driven · confidence 0.91 · traces: UCA-17, CONOPS §4.2 · awaiting human review
HOW — THE HYBRID NLP / LLM PIPELINE
Ingest program
documents
CONOPS, ORDs, threat assessments, notes
→
Find & classify
requirement content
NLP tagging + INCOSE / EARS pattern matching
→
LLM drafts
candidates
Conditioned on the program's corpus & standards
→
Deterministic gate
rejects bad drafts
Malformed, ambiguous, or conflicting — discarded
→
Human review
& promotion
Peer review gates entry into the baseline
The LLM only drafts. A deterministic rule engine rejects failures before a human ever sees them; peer review promotes the survivors — each carrying full provenance: source passage, model version, every check passed or failed. Nothing enters a safety baseline unreviewed.

## Slide 12
Traceability that maintains itself
CAPABILITY 2
LOAD LIFTED manual link bookkeeping
A knowledge graph of the whole program
Every artifact and its semantic relationships. When anything changes, embedding-based similarity proposes candidate trace links — prospectively, as artifacts evolve, not recovered after the fact.
Ontology-constrained, not free-associating
Link types are restricted to those the standards define: 882E hazard↔requirement↔mitigation; RAAML STPA↔GSN; UL 4600 evidence linkages. The graph can only assert relationships the standards recognize.
Confidence-scored, human-adjudicated
Every suggested link carries a confidence score; links below threshold are flagged for human decision, never auto-accepted.
Why it matters
Traceability is not administrative bookkeeping. It is the mechanism by which an assessor verifies that every hazard is addressed, every safety requirement is verified, and every piece of evidence connects to a claim.
Automation doesn't remove judgment — it points judgment at a comprehensive link set instead of a hand-built one.
The double tap: the DST doesn't just automate traceability — it removes the burden of carrying the link map in your head. The spreadsheet matrix, the single largest cognitive tax in safety-driven MBSE, goes away.

## Slide 13
A living safety case — that refuses to overstate itself
CAPABILITY 3
LOAD LIFTED review-time archaeology
Structural completeness
Goals without arguments, arguments without evidence, evidence without artifacts, STPA hazards without requirements — gaps surface continuously, not at review prep.
Confidence, not verdicts
Bayesian propagation from leaf evidence to top-level claim, reported as a distribution. Never a binary safe/unsafe determination — that judgment stays human.
Divergence flagging
High completeness with low confidence — evidence that exists but is weak, stale, or inconsistent — is explicitly flagged, defusing the false-confidence trap.
Irreducible review points
Where a claim is inherently engineering judgment (ODD adequacy, test coverage sufficiency, residual risk), the system requires documented human rationale and will not auto-populate confidence.
MIL-STD-882E built in: safety case elements map to the standard's required artifacts — SSPP, PHL, SHA, O&SHA, SAR — with automated tracking of what exists, is current, and carries sufficient evidence (via Shea's STPA→882E mapping).

## Slide 14
Every risk they raised, answered in the architecture
CLOSING THE LOOP
RISK (THOMAS & WAGNER, SAE 2026)
DIGITAL SAFETY TWIN MITIGATION
Hallucination (I2 impact)
LLM proposes; deterministic engine disposes. Staged promotion, peer review, immutable provenance — no AI content reaches a safety baseline unreviewed.
Over-reliance & false confidence
No safe/unsafe verdicts. Completeness, currency, and confidence reported separately; divergences flagged; irreducible review points demand documented human rationale.
Explainability for assessors
Suggestions grounded in retrievable evidence — the actual text spans and model elements shown to the reviewer. Full audit trail compatible with 882E / UL 4600, including what was rejected and why.
Skill fade & human capability
Engineers adjudicate every consequential link and promotion; effort shifts from bookkeeping to judgment, keeping verification ability exercised.
Artifact elimination
Individual tasks are automated; intermediate artifacts are preserved and linked — the SCADE lesson, applied to AI.
Unproven at scale
Phased validation with go/no-go gates: synthetic benchmarks → shadow mode beside the manual workflow → primary use with continuous measurement.

## Slide 15
What this buys a ground vehicle program
THE PAYOFF
An evidence-based answer, at any moment:
“How complete — and how confident — is our safety case, right now?”
PDR
Which STPA unsafe control actions are identified, allocated to requirements, allocated to design, verified.
CDR
Residual gaps between the committed safety case and the evidence in hand.
TRR
Whether the planned test program covers identified hazard scenarios with sufficient depth.
Structured, quantified input to a human judgment — never a pass/fail verdict.
One analysis, every framework
STPA unsafe control action
↳
MIL-STD-882E hazard — severity & probability classification
↳
UL 4600 safety case sub-goal, linked to evidence
↳
DoDD 3000.09 review artifacts, kept current
Update once — corresponding elements in the other frameworks are flagged for review automatically.
Net effect: the engineer's cognitive effort shifts from bookkeeping to judgment — the same transition that made parametric CAD succeed.

## Slide 16
Adoption is won — or lost — in the first weeks
MAKING IT STICK
The SEI found every primary MBSE barrier is cultural — and the enterprise-software world spent a decade and small fortunes proving the same lesson: adoption follows from simplifying the system, not adding features. The winning question is “why do we do it like this at all?”
Fewer tools, not another layer
Each capability eliminates something engineers already resent — the spreadsheet trace matrix, ad hoc document-to-model translation, the review-prep fire drill — rather than adding a system on top of them.
Deploy independently — start where it hurts most
Traceability, formalization, and safety case assessment each stand alone. Adopt the one that addresses the program's acutest pain point; expand incrementally from there.
Tangible effort reduction within the first iteration cycle
If engineers don't feel relief within weeks — not months — adoption stalls regardless of long-term potential. Early, visible wins are a design requirement, not a marketing goal.
Champion-led pilots generate the early proof
Shadow-mode pilots run by internal champions — beside the manual workflow, not replacing it — give the program evidence of value before it commits its baseline, and the same data feeds the go/no-go gates.
Weeks to visible value, or the long-term potential never gets its chance.

## Slide 17
Take the savings. Keep the rigor.
TAKEAWAYS
Hold AI-augmented safety tools to the same evidentiary standard as the systems they assess.
The MBSE gap is cognitive overload, not tooling — mandates outran the manual burden of traceability, formalization, and auditable safety argument.
The culture clash is resolvable: AI-community pace, bound by safety-community rigor — tool qualification, artifact preservation, engineered human oversight.
The Digital Safety Twin operationalizes that bargain: AI accelerates the mechanics; qualified engineers keep intellectual authority over every safety judgment.
The change is coming regardless — XM30-class and RCV-class safety cases will not scale on spreadsheets. Start bounded and instrumented now: the traceability discipline, provenance practices, and review workflows you build today are what any AI-augmented approach will run on.
The gap is open: no commercial MBSE tool today unifies AI hazard analysis, safety case generation, and 882E compliance in one workflow. We're working in that gap — if your program is confronting it, come compare notes.
Nelson Santini · Anoop Balakrishnan · Michael Wagner | Edge Case · mwagner@ecr.ai · find us during the symposium