## Slide 1
Heath Kouns, Marc Simms, Evan Weiss, Joe Breedlove
Moog Inc. | GVSETS 2026
Robust Fiber Optics for Ground Combat Vehicles
DISTRIBUTION STATEMENT A.
Approved for public release; distribution is unlimited.

## Slide 2
High-resolution sensors, sensor fusion, and autonomy are driving bandwidth demand
Low-latency, EMI-resilient data paths are mission critical
Network architecture is critical to future lethality
MOSA drives modular, interoperable networks
Ground Vehicles are Data Networks

## Slide 3
Copper adds weight and consumes limited vehicle space
EMI control, shielding, and grounding become harder as networks scale
As bandwidth rises, copper faces signal-integrity and scaling limits
Legacy physical layers limit future network architecture
Copper Is Becoming the Bottleneck

## Slide 4
Operators and maintainers often perceive fiber as less durable
Connector handling and contamination concerns dominate perception
Retrofit and sustainment concerns have delayed adoption
When the physical layer isn’t trusted, architecture progress stalls
The Challenge Isn’t Performance — It’s Trust
Legacy
Future

## Slide 5
Fiber in vehicle harnesses is more durable than commonly assumed
Most failures come from improper routing (micro bends), contamination, or retention and strain relief issues
Fiber failure modes differ from copper, but are not inherently worse
Radiation induced fiber darkening is not a primary concern for ground vehicles
The Problem is not the Glass

## Slide 6
Survivability Depends on System Integration
Connector
Cable
Routing
Protection
Diagnostics
Qualified parts alone do not create a robust optical network
Cable design, connector selection, routing, and diagnostics all matter
System integration determines survivability and maintainability
The right design practices turn optical advantages into operational value

## Slide 7
Bend-insensitive fibers and crush-resistant cable designs improve survivability
Reinforced cable constructions and rugged jackets protect against vehicle and operator abuse
Improved termini and interconnects reduce contamination sensitivity
Modern optical hardware is materially different from legacy telecom assumptions
Modern Optical Hardware Solves Legacy Concerns

## Slide 8
Rugged discrete and multichannel connectors harden the interconnect layer
Expanded-beam termini improve tolerance to dirt and repeated mate/demate cycles
FORJs and High-Speed Data Links preserve bandwidth across rotating interfaces
Rugged Passive Optical Building Blocks
Rugged LCs
Rugged MT
Expanded Beam
Field Installable Splices

## Slide 9
Transceivers integrated into bulkhead connectors simplify transitions for legacy copper boxes
Rugged board-level transceivers preserve standard optical interfaces while improving survivability under vehicle shock, vibration, temperature, and contamination
Ruggedized media converters and switches enable reliable Video and Ethernet links over fiber in harsh vehicle EMI environments
Rugged Active Optical Building Blocks

## Slide 10
Point-to-point: simple, direct, proven
Parallel optics: scale bandwidth by adding lanes
WDM: expand capacity with fewer fibers
Match the optical architecture to platform constraints and future growth
Choose the Right Optical Architecture

## Slide 11
Use contamination tolerant interfaces where possible
Integrate Built-In Test (BIT) and link diagnostics to speed fault isolation and provide predictive maintenance alerts
Enable field repair with splice kits and modular replacement strategies
Diagnostics and repair procedures should be part of the starting architecture
Maintainability Must Be Designed In

## Slide 12
Bandwidth is now a mission driver
Ruggedization is a system engineering discipline
Fiber is ready for broader ground vehicle adoption
Treat fiber as a backbone, not a one-for-one copper replacement
Ground Vehicles Need an Optical Backbone
The question is no longer whether fiber can survive in combat vehicles — it is where and how to deploy it for the mission.

## Slide 13
Thank you for your attention.
Contact:
Heath Kouns
hkouns@moog.com
Questions