## Slide 1
Timothy Ross, Julia Boone, Fatemeh Afghah (PhD)
Multimodal Digital-Twin Simulations for Off-Road Autonomous Vehicles
DISTRIBUTION STATEMENT A.
Approved for public release; distribution is unlimited. OPSEC # 10945
Acknowledgment: This work was supported by Clemson University’s Virtual Prototyping of Autonomy Enabled Ground Systems (VIPR-GS), under Cooperative Agreement W56HZV-21-2-0001 with the US Army DEVCOM Ground Vehicle Systems Center (GVSC).
Reference herein to any specific commercial company, product, process, or service by trade name, trademark, manufacturer, or otherwise, does not necessarily constitute or imply its endorsement, recommendation, or favoring by the United States Government or the Department of the Army (DoA).
Clemson University, Department of Electrical and Computer Engineering
Intelligent Systems and Wireless Networking (IS-WiN) Laboratory

## Slide 2
Simulation Development
DISTRIBUTION STATEMENT A.
Approved for public release; distribution is unlimited. OPSEC # 10945
Notes: We can separate simulation development into six distinct categories:
Level 0 – curation of visual and physical data sources (e.g., where are you getting your data from? Is it ‘made up’? Is it grounded in real-world data?)
Level 1- visual and physical primitives. Defines the representation of visual and physical data. The quality of this representation helps determine the quality of the simulation
Level 2 – Static Rendering, Physics, and Environmental Rendering – determines how all static properties get instantiated within the environment. This is usually handled directly by the game engine (if using one), but also involves the creation of shader + material properties
Level 3 – Sensor modeling and generation – (e.g. are your sensors based upon real, physical units? How high fidelity are they compared to the real-world?)
For everything Level 3 or below, the vehicle + sensors are the only dynamic parts of the simulation
Level 4 – Dynamic mechanics and operations – involves changing weather, lighting, friction, etc. Used to estimate real-world behaviour from static state estimation
Level 5 – Digital-Twin – involves direct bi-directional communication between simulation and real-world hardware/software
The goal of this paper is to develop a level 4 simulation for future level 5 development

## Slide 3
Level 4 Simulation Framework
DISTRIBUTION STATEMENT A.
Approved for public release; distribution is unlimited. OPSEC # 10945
Notes: We develop four primary contributions:
Simulation – what game engine, ugv models, and sensors packages do we use
Environment Generation – a simple, yet diverse procedural generation framework that transforms a set of categorical and numerical parameters into a static terrain with dynamic modeling
Data streaming – a method used for indefinite sequence duration and optimization of computational resources
Scenario Modeling – creation of metadata labels for sequence labeling

## Slide 4
Failure Sequences: support robustness evaluation
Continuous/Dynamic Scenes: support real-world long duration applications
Equivalent Benchmarks
DISTRIBUTION STATEMENT A.
Approved for public release; distribution is unlimited. OPSEC # 10945
Notes: Our simulation platform is capable of providing:
- continuous sequences (evolving dynamic weather + lighting)
- long sequences (reflective of off-road autonomous vehicle applications)
- both benign and failure designations (permits model robustness evaluation)

## Slide 5
Our primary contributions:
Simulation platform and sensor modeling
Procedural environment synthesis
Real-time multimodal data streaming
Explicit scenario modeling
Level 4 Sim Development
DISTRIBUTION STATEMENT A.
Approved for public release; distribution is unlimited. OPSEC # 10945
Notes: We present the four primary contributions

## Slide 6
Why choose Unity?
NVIDIA PhysX physics engine
Availability of community resources
Future ease for closed-loop simulations through Reinforcement Learning package, “MLAgents”
Simulation Platform and Sensor Modeling
DISTRIBUTION STATEMENT A.
Approved for public release; distribution is unlimited. OPSEC # 10945
Notes: Unity Technologies, “Unity, real-time development platform,” https://unity.com, 2026
Unity game engine chosen for:
High fidelity physics engine
Availability of resources
Proprietary RL integration for closed-loop model testing

## Slide 7
Clearpath Robotics Husky A-300
39 x 27.5 x 15” dimensions
176 lbs (80kg)
30° maximum climbing incline
Controller provided by Clemson Autodrive’s vehicle controller for preset dynamics
UnitySensors 2.0.5 (Field Robotics Japan)
Five RGB cameras (front, back, left, right, overhead)
Velodyne VLP-32 (max. 115,200 points)
GPS
IMU (velocity, acceleration, rotation, angular velocity, GT position)
Simulation Platform and Sensor Modeling
DISTRIBUTION STATEMENT A.
Approved for public release; distribution is unlimited. OPSEC # 10945
Notes: Clearpath Robotics, “Husky UGV – specification comparison,” https://clearpathrobotics.com/husky-spec-comparison/, 2026
T. V. Samak, C. V. Samak, and M. Xie, “Autodrive simulator: A simulator for scaled autonomous vehicle research and education,” in Proceedings of the 2021 2nd International Conference on Control, Robotics and Intelligent System, ser. CCRIS ’21. New York, NY, USA: Association for Computing Machinery, 2021, p. 1–5. [Online]. Available: https://doi.org/10.1145/3483845.3483846
R. Tanaka, A. Harada, and the Field Robotics Japan contributors, “Unity sensors,” https://github.com/Field-Robotics-Japan/UnitySensors, 2025
UGV Choice:
Clearpath Robotics Husky A-300 is a small vehicle with intentionally limited mobility; permits the study of navigation and path planning
UnitySensors 2.0.5:
Primary sensors package
Use of overhead RGB camera permits study of multi-agent decision making

## Slide 8
Four primary components: heightmaps, surfaces, objects, environmental conditions
Procedural Environment Generation
Mountainous Region
Heightmaps generated using noise functions like Perlin, Simplex, and Cellular
Desert Region
DISTRIBUTION STATEMENT A.
Approved for public release; distribution is unlimited. OPSEC # 10945
Notes: Clearpath Robotics, “Husky UGV – specification comparison,” https://clearpathrobotics.com/husky-spec-comparison/, 2026
T. V. Samak, C. V. Samak, and M. Xie, “Autodrive simulator: A simulator for scaled autonomous vehicle research and education,” in Proceedings of the 2021 2nd International Conference on Control, Robotics and Intelligent System, ser. CCRIS ’21. New York, NY, USA: Association for Computing Machinery, 2021, p. 1–5. [Online]. Available: https://doi.org/10.1145/3483845.3483846
R. Tanaka, A. Harada, and the Field Robotics Japan contributors, “Unity sensors,” https://github.com/Field-Robotics-Japan/UnitySensors, 2025
Different heightmaps can be generated using different numerical/categorical parameters into different noise functions

## Slide 9
Procedural Environment Generation
Four primary components: heightmaps, surfaces, objects, environmental conditions
Surface textures are:
Blended using splatmap arrays
Assigned friction (‘stiffness’) values to align with terramechanic properties
DISTRIBUTION STATEMENT A.
Approved for public release; distribution is unlimited. OPSEC # 10945
Notes: Surface are:
Instantiated based upon height value
Blended to provide smooth transitions
Diversified using flood-fill algorithms to support unique path-planning scenarios
Integrated with physics engine using Unity’s WheelFrictionCurve object that is assigned to each Unity WheelCollider

## Slide 10
Procedural Environment Generation
Four primary components: heightmaps, surfaces, objects, environmental conditions
Objects are:
Spawned according to user-defined density, size, distribution rules
Programmatically limited to physically plausible regions
Environmental Conditions are:
Generated using GPU instantiating
Interpolated using weather controller to provide plausible transitions
DISTRIBUTION STATEMENT A.
Approved for public release; distribution is unlimited. OPSEC # 10945
Notes: Objects are:
Distributed according to simple noise functions that have similar numerical/categorical parameters to those used in heightmap generation
Contain additional parameters to control appearance and density (height, width, prevalence, etc.)
Bounded by surface-defined regions (trees cannot spawn in lake)
Environmental Conditions are:
Optimized for simulation performance using GPU instantiating
Interpolated using weather controller (ex. Fog-to-Sunny: automatically interpolates fog density, cloud opacity, etc.)

## Slide 11
Real-Time Multimodal Data Streaming
Objective: alleviate computational workload by offloading data storage
System RAM
Data Buffer
Client
Once full, async buffer flush
Cam 4 Data
Cam 1 Data
Parse and store data
System SSD
Server
DISTRIBUTION STATEMENT A.
Approved for public release; distribution is unlimited. OPSEC # 10945
Notes: Permits indefinite data collection
Utilizes dual-machine approach
Unity-running system allocates data buffer for temporary storage
Asynchronously flushes buffer to other machine when buffer is full
Async flushing is necessary to prevent simulation buffering

## Slide 12
Real-Time Multimodal Data Streaming
Sensor Data Packet Organization
Pipeline may also be used for sending simulation metadata:
fault designation
weather
time-of-day
DISTRIBUTION STATEMENT A.
Approved for public release; distribution is unlimited. OPSEC # 10945
Notes: Packet is organized for easy parsing by data storage client
Introductory packet used to send current and future simulation metadata (weather conditions, lighting conditions, etc.)
Final packet used to identify fault designation

## Slide 13
Scenario Modeling
Weather State | Description
Clear | Minimal cloud; negligible wind
*Foggy | Visibility is significantly limited
*HeavyRain | Dense precipitation and significant wind
*LightRain | Moderate rain and light wind
Scattered | Moderate cloud distribution
Time of Day | Solar Elevation
Day | 10° < θ ≤ 170°
Dusk | 170° < θ ≤ 190°
*Night | 190° < θ ≤ 350°
Dawn | 350° < θ ≤ 10°
Fault Designation | Description
Benign | Expected traversal
Collision | Vehicle experience collision
Epistemic | Terrain-induced mobility
Water | Immobilized by water plane
Weather-Associated | Non-benign with adverse weather
DISTRIBUTION STATEMENT A.
Approved for public release; distribution is unlimited. OPSEC # 10945
Notes: Adverse conditions (Foggy, HeavyRain, LightRain) used to define weather-associated fault designation (any non-benign weather condition caused by visual degradation from adverse weather)

## Slide 14
Domain Examples
Seeds allow for semantically equivalent, but spatially diverse environments
DISTRIBUTION STATEMENT A.
Approved for public release; distribution is unlimited. OPSEC # 10945
Notes: Set of seven environments defined to demonstrate simulation diversity; simultaniously creates unique challenges
Ex:
NormalForest used as baseline for object identification, scene segmentation
Desert used for elevation-based path planning
Wetlands used for aerial navigation during ground-view camera occlusions
Lakes used to determine ground-based segmentation with respect to challenging water reflections

## Slide 15
Domain Examples
Applicable tasks:
Object Detection
Scene Segmentation
Multi-agent Decision Making
Path Planning
Localization
DISTRIBUTION STATEMENT A.
Approved for public release; distribution is unlimited. OPSEC # 10945
Notes: Example of ground and aerial samples from each environment
In future work, we intend to provide full-suite of tasks of benchmark tasks for each domain

## Slide 16
Data Curation Presets
Include short (20s), medium (180s), and long (1,500s) duration sequences
Permit weather changes in medium + long sequences
Manually teleoperate vehicle. Designate failure cases
DISTRIBUTION STATEMENT A.
Approved for public release; distribution is unlimited. OPSEC # 10945
Notes: Small set of data samples collected using expressed presets

## Slide 17
Future Work
Improvements to mesh colliders for LiDAR raycast collisions
Improved terramechanic fidelity for dynamic friction surfaces
DISTRIBUTION STATEMENT A.
Approved for public release; distribution is unlimited. OPSEC # 10945
Notes: LiDAR Collisions:
Current approach (GPU instantiated grass objects) does not have proper LiDAR collisions, since the grass blades do not have colliders
Switch to mesh-based ray casting could provide improved accuracy
Exploration into LiDAR impact during adverse weather (HeavyRain)
Terramechanic fidelity:
Friction surfaces generally modeled upon real-world data, but not entirely accurate
Need for additional terramechanic modeling (ex. sand deposit deformation when traversing)