## Slide 1
Author: Rupert Tull de Salis1, PE, MEng, MSc
Presenter: Wiktor Dotter, CEO powersize.tech
PARAMETRIC SCREENING OF HYBRID POWERTRAIN ARCHITECTURES FOR HIGH-ENERGY LASER VEHICLES: APPLICATION TO FOXHOUND AND BOXER

## Slide 2
1. Motivation and Context
2. The Two Platforms: Foxhound and Boxer
3. HEL Classification: Classes A-E
4. Power and Mass Drivers (WPE, Thermal Management)
5. Engagement Cycle and Sustained Firing Fraction
6. HEL Electrical Demand and Mass by Class
7. Analysis Methodology: CEMP-H and powersize.tech
8. Parallel vs. Series Architectures
9. Results: Foxhound
10. Results: Boxer
11. Discussion: Synergies of Hybridization
12. Conclusions
Contents

## Slide 3
The threat:
Drone swarms dominate battlefield air threat;
HEL offers unlimited magazine, low cost per engagement, high sustained fire rate
Recent commitments:
US Army: 50 kW DE M-SHORAD on Stryker; 300 kW-class IFPC-HEL program.
UK MoD: ~£1 billion committed for DEW in 2025 Strategic Defence Review.
DragonFire ordered for Royal Navy.
The gap:
No published methodology for matching a HEL to a vehicle platform at concept stage, before weapon or vehicle parameters are frozen
This paper:
Introduces A-E HEL classification; estimates power and mass by class; screens hybrid powertrain architectures for Foxhound and Boxer using powersize.tech
Motivation and Context
Directed Energy Maneuver Short-Range Air Defense (DE M-SHORAD) 50 kW-class laser weapon system mounted on a Stryker A1 8×8 armored vehicle.
(U.S. Army photograph, public domain, DVIDS 9107830)

## Slide 4
Foxhound LPPV (Light Protected Patrol Vehicle)
GVM: 7,500 kg | Max payload: ~2,000 kg | Engine: Steyr M16, 160 kW
Smallest British Army vehicle that could support a functional HEL
GVM ceiling is hard: higher GVM requires different driving licence in UK/Europe
Boxer MIV 8x8 (Mechanised Infantry Vehicle)
GVM: 38,500 kg | Payload: 15,000 kg (mission module)
Engine: MTU, 600 kW
623 vehicles on order (£2.8 billion); interchangeable mission modules
German Bundeswehr has ordered Skyranger 30 HEL (~50 kW near-term target) on Boxer chassis
The Two Platforms:
Foxhound and Boxer
Upper Slide: Photo: U.S. Army / DVIDS, public domain
Lower Slide: Photos: © Crown Copyright 2012 OGL; GTK Boxer, public domain
Notes: Table 1 (paper): Platform payload budget for HEL integration.
Images:
Foxhound Light Protected Patrol Vehicle (LPPV) at Camp Bastion, Helmand Province, Afghanistan, June 2012. Photo: Sgt Andy Reddy RLC. © Crown Copyright 2012. Licensed under the Open Government Licence v1.0 (OGL v1.0). Source: UK Defence Imagery / Wikimedia Commons.
GTK Boxer 8×8 armoured vehicle (German Army). Photo: Heldt. Public domain. Source: Wikimedia Commons.

## Slide 5
No standard taxonomy of HEL classes exists in published literature. This paper proposes one.
HEL Classification: Classes A-E
 | Maximum Output Power, kW | Target | Defeat Method
Class A | 30 | Light UAS/quadcopters | Soft kill: Sensor/electronics burn-out; thin plastic/composite skin ignition
Class B | 60 | Fixed-wing UAS/ loitering munitions | Soft kill: Warhead cook-off or control surface damage; fuselage skin penetration
Class C | 150 | Rotary-wing USA and light armored vehicles | Hard kill: Rotor blade severance; thin steel skin penetration and internal component destruction
Class D | 300 | Helicopters and fast jets | Hard kill: Airframe structural failure; fuel ignition through skin burn-through
Class E | 500 | Maximum ground vehicle scenaion | Hard kill: Thick steel armor penetration; structural failure of heavy vehicles
Derivation method:
Fluence-to-kill thresholds by target type (Zohuri 2016)
Cross-validated against open-source program evidence (known systems vs. target types defeated)
Class boundaries drawn at qualitative capability steps
Notes: Table 3 (paper): Full class framework with program references and defeat mechanisms
Ballistic missile intercept (>500 kW) excluded: impractical for beam propagation and aiming from ground vehicles, as the distance to airborne objects is too great for precision aiming.

## Slide 6
Wall-Plug Efficiency (WPE):
Laboratory (laser head only): 50-56% Installed (full system incl. PTMS): ~33%
No improvement trend in field data (2015-2025)
Gap explained by: chiller, pumps, compressors, controls billed to a separate circuit
Power and Thermal Management System (PTMS) - the dominant mass item:
Absorbs burst waste heat during firing (phase-change material thermal store)
Rejects cycle-average heat during recovery (vapor-compression chiller)
Cannot use ram-air / low-temperature air (unlike aircraft) - active chiller required to 49°C
Chiller specific mass: 4.0-5.5 kg/kW(thermal)
Laser source specific mass: 4-5 kg/kW - also no improvement trend across all power classes and years
Power and Mass Drivers:
WPE and Thermal Management
Wall Plug Efficiency (output power / input power, %)
HEL Specific Mass (kg/kW)
Notes: Key implication: Cannot wait for the technology to mature - must design for current values.

## Slide 7
Three-phase engagement cycle:
1. Firing phase: laser on, high power draw, waste heat generated
2. Re-acquire phase: beam slews to next target (several seconds)
3. Thermal recovery: PTMS drains phase-change store; laser off, chiller at full load
SFF = fraction of total cycle time during which the laser fires
Upper bound: SFF = 83% (DragonFire dwell time; zero recovery time assumed)
Adopted value / tactical floor: SFF = 50% (a system in recovery >50% of the time lacks tactical utility)
Ultracapacitors smooth the power demand:
High power density, short duration: ideal fit for firing/recovery cycle
Class E example: two Skeleton SkelMod modules, 70 kg, store 417 Wh - negligible added mass
Vehicle need only supply average power, not firing peak
Engagement Cycle and
Sustained Firing Fraction (SFF)
Power demand for HEL system. Alternating firing and thermal recovery, for SFF = 50%.
This power demand can be smoothed to a near-constant average value, by the use of ultracapacitors.

## Slide 8
Two simultaneous constraints the powertrain must satisfy for each HEL class:
1. Average electrical demand (kW) during engagement phase
Dominant loads: laser chain + chiller (both scale with class);
beam director + sensors (fixed)
Chiller COP: 3.7 (Carnot analysis, cross-validated against published
vapor-compression data)
Installed system WPE converges at Class C+ as chiller dominates;
fixed loads matter at Class A
2. Installed system mass (kg)
Laser source: 4-5 kg/kW
PTMS: 4.0-5.5 kg/kW(thermal), at cycle-average waste heat rejection rate
EPS on series hybrid: 0.5-1.0 kg/kW (DC bus already present; AC front-end eliminated)
Beam director and fixed systems: approximately constant across class
HEL Electrical Demand
and Mass, by Class
HEL System Mass (kg) versus Operational Power Draw (kW).
Notes: Table 5 (paper): Electrical demand and system WPE by class
Table 6 (paper): Installed HEL mass range by class

## Slide 9
CEMP-H Mission Profile:
24-hour charge-neutral cycle: 5 hr Silent Watch | 2 hr Silent Mobility | 1 hr weapons engagement | base-rest Export Power
Average HEL electrical demand added as continuous DC load during the 1-hour engagement phase
Powersize.tech - rapid parametric powertrain screening:
Inputs: vehicle mass, rolling resistance, drag, frontal area, max speed, electrical loads, Export Power
No detailed BSFC maps required - concept-stage open-source data only
Output: minimum engine power, battery capacity, component masses and costs
Component sizing - sequential efficiency cascade:
Series chain: engine → MGU → rectifier → inverter → traction motor → driveline
Each stage derated by component-class efficiency from powersize.tech database
Engine power floor: no lower than current platform spec (160 kW Foxhound / 600 kW Boxer)
Analysis Methodology: CEMP-H and powersize.tech
Notes: CEMP mission profile is a new profile for tactical wheeled vehicles, proposed in the paper.

## Slide 10
Both architectures sized. Series hybrid selected for HEL integration.
Parallel hybrid:
Engine and motor both connect mechanically to driveline
Engine operating point constrained by traction demand - HEL load not fully decoupled
Lower mass and cost - used as reference baseline in Tables 7 and 8
Series hybrid:
Engine drives generator only; wheels driven electrically
Engine, traction, and HEL loads fully decoupled - each optimised independently
High-voltage DC bus already standard in drivetrain
HEL EPS reduces to DC-DC converter + EMI filter only (AC front-end eliminated)
EPS mass: 0.5-1.0 kg/kW vs. 1.0-2.0 kg/kW for standalone diesel-generator EPS
Parallel vs. Series Hybrid Architecture
Parallel-Hybrid Architecture with HEL Power Output
Series-Hybrid Architecture with HEL Power Output
Notes: Batteries for Silent Watch/Mobility also support limited HEL operation with engine off

## Slide 11
Foxhound evaluated for Classes A, B, C only (payload constraint).
Minimum retained payload: 240 kg (driver + gunner at 95th percentile NATO male + kit)
ICE baseline:
160 kW engine; 2,000 kg payload available for HEL system + powertrain additions
Step 1 - Series hybridization (no HEL):
+1,126 kg powertrain addition; assumes weight savings elsewhere preserve 2,000 kg payload target
Step 2 - Add HEL:
Class A (30 kW): minimal engine change; small mass addition; payload comfortable
Class B (60 kW): minimal engine change; payload remains viable
Class C (150 kW): engine uprate to 228 kW required; +274 kg; feasible only if HEL mass near lower estimate
Results: Foxhound LPPV
System Mass (kg) versus HEL Class – Foxhound
Notes: Table 7 (paper): Full specifications and mass for all Foxhound configurations

## Slide 12
Boxer evaluated for Classes C, D, E. Payload: 15,000 kg.
Weight is not the limiting factor.
ICE baseline:
600 kW engine; 15,000 kg mission module payload available
Step 1 - Series hybridization (no HEL):
Substantial powertrain addition; payload margin remains very large
Step 2 - Add HEL:
Class C (150 kW): no engine uprate required; payload impact manageable
Class D (300 kW): no engine uprate required; payload comfortably within budget
Class E (500 kW): engine uprate to 704 kW required; still within payload budget
704 kW and 228 kW (Foxhound Class C) are both commercially available engines.
Results: Boxer MIV
System Mass (kg) versus HEL Class – Boxer
Notes: Table 8 (paper): Full specifications and mass for all Boxer configurations

## Slide 13
The series hybrid creates compound value for HEL integration:
1. Engine fully decoupled from HEL and traction - no interference between demands
2. DC bus already present - HEL EPS is only DC-DC converter + EMI filter
Saves 0.5-1.0 kg/kW in EPS mass vs. standalone EPS; saving scales with class
3. Batteries sized for Silent Watch / Mobility support limited HEL with engine off
Foxhound: 65 kWh | Boxer: 210 kWh
4. If engine power is insufficient, mitigation options:
Reduce SFF below 50% | Reduce chiller size (accept de-rating at high ambient temperature)
Seek improved WPE from laser supplier | Reduce target laser output class
Conclusion:
If Hybridized for Silent Watch and Silent Mobility, HEL integration comes at low incremental cost.
Discussion: Synergies of Hybridization

## Slide 14
1. Novel HEL classification (Classes A-E):
Defined by target type and laser output, 30-500 kW; covers all ground vehicle scenarios
2. Foxhound in series hybrid form:
Supports Class A-B with minimal powertrain modification (CEMP-H spec for Silent Watch/Mobility assumed). Class C attainable with engine uprate to 228 kW.
3. Boxer in series hybrid form:
Supports Class C-D within payload and existing engine power. Class E (500 kW) attainable with engine uprate to 704 kW.
4. powersize.tech enables concept-stage analysis:
Open-source vehicle data only; no specialist simulation expertise; multiple HEL classes and platforms screened simultaneously
5. Series hybrid is the preferred host architecture:
DC bus synergy reduces EPS mass; batteries support silent HEL engagement; HEL integration cost is incremental.
Conclusions

## Slide 15
Questions
Notes: Rupert Tull de Salis, PE, MEng, MSc
ZeBeyond Ltd, Leamington Spa, UK
rdesalis@umich.edu
www.linkedin.com/in/rupert-de-salis
Full paper preprint (with appendices):
DOI: 10.5281/zenodo.19113766
Companion paper (CEMP-H mission profile and workbooks):
DOI: 10.5281/zenodo.19113638
ePOP Concept: ZeBeyond Ltd | www.zebeyond.co.uk
DISTRIBUTION STATEMENT A. Approved for public release; distribution is unlimited.